## Slide 1: Diagnostic Radiology Residents Physics Curriculum Q&A November 2013
Imaging Physics Curricula Subcommittee
AAPM Subcommittee of the Medical Physics Education of Physicians Committee
Supported by: AAPM Education Council and the Academic Council of the Association of
University Radiologists

## Slide 2: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 3: Structure of the Atom
Q1. The maximum number of electrons in the outer shell of an atom is:
A. 2n2
B. 8
C. 16
D. 32
E. 2

## Slide 4: Structure of the Atom
Q2. Elements which have the same Z (atomic number) but different A (mass number) are called:
A. isobars
B. isomers
C. isotones
D. isotopes

## Slide 5: Structure of the Atom
Q3. The mass number (A) of an atom is equal to the sum of the:
A. neutrons
B. protons
C. neutrons and protons
D. protons and electrons
E. atomic masses plus the total binding energy

## Slide 6: Structure of the Atom
Q4. The binding energy of an electron in the K-shell is:
A. the energy the electron needs to stay in the K-shell
B. the energy needed for an electron to make a transition to the L-shell from the K-shell
C. the energy needed for an electron to jump from the L-shell to K-shell
D. the energy needed to remove an electron from the K-shell
E. none of the above

## Slide 7: Structure of the Atom
Q5. A proton is electrostatically repelled by:
A. electrons
B. neutrons
C. positrons and neutrons
D. alpha particles and electrons
E. positrons and alpha particles

## Slide 8: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 9: Electromagnetic (EM) Radiation
Q1. All but which of the following modalities uses electromagnetic radiation during diagnostic imaging procedures.
A. fluoroscopy
B. mammography
C. MRI
D. ultrasound
E. CT

## Slide 10: Electromagnetic (EM) Radiation
Q2. Electromagnetic radiation can be categorized as either ionizing or non-ionizing radiation. The principle characteristic that determines this function is:
A. wavelength
B. frequency
C. energy
D. speed
E. transmission media

## Slide 11: Electromagnetic (EM) Radiation
Q3. The electromagnetic spectrum is a continuum of electric and magnetic energies that vary in wavelength and frequencies. Identify which of the following are utilized in diagnostic imaging:
A. radiofrequency, infrared, visible light
B. infrared, visible light, UV
C. radiofrequency, visible light, X-ray
D. ultraviolet, x-ray, gamma rays
E. x-rays, gamma rays

## Slide 12: Electromagnetic (EM) Radiation
Q4. Historically, different forms of electromagnetic radiation have been used in medical imaging to identify abnormalities. Except for one category, all of the following have been used for breast imaging. Identify that category.
A. radiofrequency
B. infrared
C. visible light
D. ultraviolet
E. gamma rays

## Slide 13: Electromagnetic (EM) Radiation
Q5. The electromagnetic spectrum is a continuum of electric and magnetic energies that vary in wavelength and frequencies. Identify which of the following are classified as ionizing radiation.
A. radiofrequency, Infrared, visible light
B. infrared, visible light, UV
C. radiofrequency, visible light, X-ray
D. ultraviolet, x-ray, gamma rays
E. x-rays, gamma rays

## Slide 14: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 15: Particulate Radiation
Q1. Which of the following is an example of high linear energy transfer (LET) particulate radiation? Note: Assume all energies are in the diagnostic range (roughly, 00.5 MeV)
A. microwaves
B. electron beam
C. proton beam
D. gamma rays

## Slide 16: Particulate Radiation
Q2. The energy of each photon created when a positron almost at rest interacts with an electron in an annihilation reaction is:
A. 5 eV
B. 144 keV
C. 511 keV
D. 1 MeV
E. 3 MeV

## Slide 17: Particulate Radiation
Q3. The Bragg peak is associated with:
A. electrons
B. x-rays
C. microwaves
D. protons

## Slide 18: Particulate Radiation
Q4. In the event of an I-131 spill (non-liquid) which of the organs below is at greatest risk of deterministic damage?
A. skin
B. brain
C. liver
D. heart

## Slide 19: Particulate Radiation
Q5. Place the following in increasing order of damage to tissue?
A. electron, neutrino, proton (100 keV), photon (diagnostic energy)
B. photon (diagnostic energy), electron, proton (100 keV), neutrino
C. neutrino, photon (diagnostic energy), electron, proton (100 keV)
D. proton (100 keV), neutrino, photon (diagnostic energy), electron

## Slide 20: Particulate Radiation
Q6. A pancake meter records dose when unshielded detector is swept over a spill, but no dose when a shielded detector is swept over the spill. What does this tell us about the spilled substance?
A. The substance is not radioactive since it did not register in both orientations
B. The substance emits high-energy photons since it only registered when unshielded
C. The substance emits particulate radiation or very low-energy photons since it only registered when unshielded
D. The substance has a very long half-life because the meter did not register when shielded

## Slide 21: Particulate Radiation
Q7. A person accidentally imbibes an unknown radioactive substance and lives in close proximity with his or her family for several hours before realizing the mistake and going to the hospital. Which of the following types of radiation is the greatest safety concern for the family?
A. photons (300 keV)
B. protons
C. electrons (30 keV)
D. alpha particles

## Slide 22: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 23: Interactions of Ionizing Radiation with Matter
Q1. The predominant interaction of 120 kVp x-rays from a computed tomography scanner with soft tissue is:
A. coherent scattering
B. Compton scattering
C. photoelectric effect
D. pair production

## Slide 24: Interactions of Ionizing Radiation with Matter
Q2. If a radiologic technologist increases the kVp from 70 to 90 during an AP projection of the lumbar spine, which of the following interactions will be the predominant interaction with bone during imaging with 90 kVp x-rays?
A. coherent scattering
B. Compton scattering
C. photoelectric effect
D. pair production

## Slide 25: Interactions of Ionizing Radiation with Matter
Q3. During imaging of a patient, the amount of Compton scatter is increased by increasing which of the following technical parameters?
A. exposure time
B. focal spot size
C. kVp
D. Source-to-image receptor distance (SID)

## Slide 26: Interactions of Ionizing Radiation with Matter
Q4. Which of the following interactions is primarily responsible for patient dose in diagnostic imaging?
A. coherent scattering
B. Compton scattering
C. photoelectric effect
D. pair production

## Slide 27: Interactions of Ionizing Radiation with Matter
Q5. The predominant interaction of Tc-99m photons with a sodium iodide crystal is
A. coherent scattering
B. Compton scattering
C. photoelectric effect
D. pair production

## Slide 28: Interactions of Ionizing Radiation with Matter
Q6. The unit for Linear Energy Transfer (LET) is
A. keV per µm
B. keV per density
C. keV per mg
D. keV per g

## Slide 29: Interactions of Ionizing Radiation with Matter
Q7. Which of the following is primarily responsible for patient dose with Iodine–131 imaging and treatment?
A. alpha particles
B. beta particles
C. gamma rays
D. neutrons

## Slide 30: Interactions of Ionizing Radiation with Matter
Q8. The occurrence of a sharp increase in photoelectric absorption is related to which of the following factors?
A. A sharp increase in photoelectric absorption occurs as density increases.
B. A sharp increase in photoelectric absorption occurs as density decreases.
C. A sharp increase in photoelectric absorption occurs when the photon energy is just above the atomic number of the substance.
D. A sharp increase in photoelectric absorption occurs when the photon energy is just above the electron binding energy.

## Slide 31: Interactions of Ionizing Radiation with Matter
Q9. A radiologic technologist uses 30 mAs and 80 kVp for an AP pelvis radiograph on a pregnant patient. What is the radiation dose to an embryo located 9 cm below the anterior surface, as expressed as a percentage of the entrance skin dose?
A. The embryo radiation dose is equal to 100% of the entrance skin dose.
B. The embryo radiation dose is equal to 50 to 75% of the entrance skin dose.
C. The embryo radiation dose is equal to 12.5 to 25% of the entrance skin dose.
D. The embryo radiation dose is equal to 1 to 3% of the entrance skin dose.

## Slide 32: Interactions of Ionizing Radiation with Matter
Q10. Which of the following is the most penetrating of the radiations listed?
A. photons from a 140 kVp x-ray beam
B. photons from Tc-99m radioactive decay
C. beta particles from F-18 radioactive decay
D. photons from F-18 radioactive decay

## Slide 33: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 34: Radiation Units
Q1. The Joint Commission sentinel event criteria require estimation of:
A. effective dose
B. equivalent dose
C. average dose
D. peak skin dose
E. integral dose

## Slide 35: Radiation Units
Q2. The ACR Appropriateness Criteria Relative Radiation Level Scale is given in units of:
A. R/min
B. mGy
C. mR
D. mSv

## Slide 36: Radiation Units
Q3. The absorbed dose multiplied by a weighting factor appropriate for the type of radiation is:
A. Integral absorbed dose
B. Equivalent dose
C. Effective dose
D. Committed equivalent dose

## Slide 37: Radiation Units
Q4. The absorbed dose to the ovaries from a limited CT exam of 8 cm length, with a 2 cm thickness contiguous acquisition with the ovaries in the beam, is 8 mGy. If the study is expanded in length to cover 16 cm instead, which of the following descriptors of dose is correct?
A. The dose to the ovaries is 16 mGy.
B. The effective dose is 8 mSv.
C. The equivalent dose is 8 mSv.
D. The imparted energy is unchanged.

## Slide 38: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 39: X-ray Production
Q1. There are various dose-saving steps a fluoroscopist can take to reduce patient dose during interventional radiology procedures. Which of the following steps will increase patient radiation dose?
A. remove grids if the patient size is small
B. select more added filtration
C. use virtual collimation to adjust collimator blades
D. select a magnified FOV
E. reduce the pulse rate in pulsed fluoroscopy

## Slide 40: X-ray Production
Q2. The following pediatric airway radiograph was obtained in the 1.5X geometric magnification mode. Which of the following is the most critical factor to ensure optimal spatial resolution?
A. added filtration
B. high kVp
C. 0.3 mm focal spot size
D. large SID (source-to-image receptor distance)
E. high mAs

## Slide 41: X-ray Production
Q3. For a dedicated chest radiographic room, the X-ray tube for the wall stand should be set with:
A. the anode side up and the cathode side down
B. the anode side down and the cathode side up
C. either anode up or down, it makes no difference in chest image quality
D. whether anode up or down depends on patient size
E. whether anode up or down depends on radiologist’s preference

## Slide 42: X-ray Production
Q4. A direct result from adding additional filters to a diagnostic X-ray beam is that:
A. the characteristic radiation is removed
B. the image contrast is improved
C. the maximum photon energy is increased
D. the X-ray tube heat loading is reduced
E. the patient dose is reduced

## Slide 43: X-ray Production
Q5. The design of a dedicated mammography unit includes tilting the x-ray tube in a special way in order to have the central axis beam positioned at the chest wall. What is the main advantage for such a unique design?
A. to reduce heel effect and improve x-ray uniformity
B. to improve heat capacity
C. to include more breast tissues against chest wall
D. to reduce patient dose
E. to improve spatial resolution

## Slide 44: X-ray Production
Q6. The appropriate focal spot size for an x-ray tube is always a trade-off between ________
and .
field of view, geometric unsharpness
patient dose, field of view
heat capacity, parallax
heat capacity, geometric unsharpness
resolution, latitude

## Slide 45: X-ray Production
Q7. When purchasing a new mobile radiographic system, one needs to consider the X-ray generator power rating. What would be the appropriate X-ray generator power rating for an imaging center that covers various adult clinical applications including chest, abdomen, pelvis, skull, and extremities.
100 – 499 watts
500 – 999 watts
1000 – 4999 watts
5000 – 10,000 watts
above 10,000 watts

## Slide 46: X-ray Production
Q8. Geometric unsharpness increases with
moving a patient close to the image receptor
increased focal spot size
longer exposure time
lower kVp
more added filtration

## Slide 47: X-ray Production
Q9. The patient skin dose will be reduced by using:
more added filtration
higher grid ratio
lower kVp
smaller focal spot size
none of the above

## Slide 48: X-ray Production
Q10. Heel effect is more pronounced when:
the image receptor is farther from the focal spot
using a large focal spot size
using a smaller image size
using no grid
using an X-ray tube with a smaller target angle

## Slide 49: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 50: Basic Imaging Science and Technology
Q1. The image of the CT phantom (displayed here) is used to measure which image property?
A. spatial resolution
B. noise
C. dose
D. temporal resolution

## Slide 51: Basic Imaging Science and Technology
Q2. The limiting resolution is to the modulation transfer function as the standard deviation of image intensities in a region of interest is to:
A. contrast-detail image
B. detective quantum efficiency
C. noise equivalent quanta
D. noise power spectrum (Wiener spectrum)
E. signal-to-noise ratio

## Slide 52: Basic Imaging Science and Technology
Q3. The CT image shown here is viewed at a window width of 30 HU and level of 20 HU. What change should be made to make the image contrast of the brain tissues more visible?
A. increase window width
B. decrease window width
C. increase window level
D. decrease window level

## Slide 53: Basic Imaging Science and Technology
Q4. What parameter change is the most likely cause of the increased noise and decreased resolution in the images above?
A. different kVp
B. different mAs
C. different gantry angle
D. different convolution kernel/filter

## Slide 54: Basic Imaging Science and Technology
Q5. Which histogram region corresponds to soft tissue in the CT image shown here?

## Slide 55: Basic Imaging Science and Technology
Q6. Given the original image (top left) and its Fourier Transform (top middle) which of the images corresponds to altering the Fourier Transform as demonstrated in the top right figure?

## Slide 56: Basic Imaging Science and Technology
Q7. The definition of segmentation in medical image processing is:
A. reduction of pixel intensity variations by averaging adjacent pixels
B. identification of the pixels which compose a structure of interest in an image
C. eliminating low spatial frequencies from the image
D. altering the relative intensities of the image pixels

## Slide 57: Basic Imaging Science and Technology
Q8. Detection of a large, low-contrast object in a noisy image can be improved by:
A. applying edge enhancement
B. applying image smoothing
C. increasing window width
D. digitally magnifying the image

## Slide 58: Basic Imaging Science and Technology
Q9. The CT image here is:
A. MIP
B. surface render
C. volume render
D. MPR
E. fused image

## Slide 59: Basic Imaging Science and Technology
Q10. You are evaluating a new diagnostic test. The yellow curve represents the histogram of patients confirmed as normal, and the gray curve represents the histogram of patients that are diseased. The test decision threshold is displayed below in blue, and everything above the threshold is called disease by the new diagnostic test. Which region(s) contains true positive results?
A. A and B
B. B and C
C. C and D

## Slide 60: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 61: Biological Effects of Ionizing Radiation
Q1. Which of the following has the highest LET?
A. alpha particle
B. gamma ray
C. x-ray
D. beta particle

## Slide 62: Biological Effects of Ionizing Radiation
Q2. Radiation-related factors that determine the biological effects of radiation include all but one of the following:
A. absorbed dose
B. dose rate
C. DNA repair mechanisms
D. type and energy of radiation

## Slide 63: Biological Effects of Ionizing Radiation
Q3. What cell type is most sensitive to radiation injury?
A. erythroblast
B. erythrocyte
C. myocyte
D. hepatocyte

## Slide 64: Biological Effects of Ionizing Radiation
Q4. What molecule is the primary site of radiation-induced injury?
A. deoxyribonucleic acid
B. ribonucleic acid
C. DNA polymerase
D. hemoglobin

## Slide 65: Biological Effects of Ionizing Radiation
Q5. Which of the following is a Non-deterministic (stochastic) biologic effect of radiation?
A. hair loss
B. skin erythema
C. cataract
D. risk of cancer

## Slide 66: Biological Effects of Ionizing Radiation
Q6. What would be a lethal dose of whole body radiation?
A. 10 Gray
B. 1 Gray
C. 0.1 Gray
D. 0.01 Gray

## Slide 67: Biological Effects of Ionizing Radiation
Q7. Pulmonary CT angiogram to assess the presence of pulmonary emboli in a 28-year-old woman who was 30 weeks pregnant would most likely increase the risk to the fetus of which of the following:
A. fetal malformation
B. prenatal death
C. childhood cancer
D. cataracts

## Slide 68: Biological Effects of Ionizing Radiation
Q8. What is the most radiosensitive organ in a young adult woman 24 years of age?
A. breast
B. lung
C. ovary
D. skin

## Slide 69: Biological Effects of Ionizing Radiation
Q9. What dose-response model does the BEIR VII report recommend for calculating the risk of biologic effects from ionizing radiation?
A. linear-quadratic
B. linear, threshold
C. linear, no threshold
D. radiation hormesis

## Slide 70: Biological Effects of Ionizing Radiation
Q10. What percentage of excess cases of cancer would you expect in a general population in the USA if 10,000 people were exposed to 10 mSv over one year from a slow radiation leak?
A. <30 percent
B. <3 percent
C. <0.3 percent
D. <0.03 percent

## Slide 71: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 72: Radiation Protection and Associated Regulations
Q1. The recommended weekly effective dose limit for radiologists under current regulations is:
A. 10 mSv
B. 50 mSv
C. 100 mSv
D. 0.5 mSv
E. 1.0 mSv

## Slide 73: Radiation Protection and Associated Regulations
Q2. According to NCRP Reports 93 (1987) and 160 (2009), over time the yearly level of background/ natural radiation received per capita has most nearly:
A. increased by a factor of two
B. increased by a factor of four
C. increased by a factor of six
D. stayed the same
E. decreased

## Slide 74: Radiation Protection and Associated Regulations
Q3. According to NCRP Reports 93 (1987) and 160 (2009), the effective dose received by the average American from medical radiation has, over time, most nearly:
A. increased by a factor of two
B. increased by a factor of four
C. increased by a factor of six
D. stayed the same
E. decreased

## Slide 75: Radiation Protection and Associated Regulations
Q4. For a janitor’s closet adjacent to a radiographic room, the shielding calculation design goal is:
A. 50 mSv per year
B. 1 mSv per week
C. 0.02 mSv per week
D. 0.1 mSv per week

## Slide 76: Radiation Protection and Associated Regulations
Q5. The ICRP released a statement in 2011 stating that the dose threshold for radiation-induced cataracts was (increased/decreased) from 2 Gy to __________.
A. increased, 3 Gy
B. increased, 4 Gy
C. increased, 8 Gy
D. decreased, 0.5 Gy
E. decreased, 0.5 mGy

## Slide 77: Radiation Protection and Associated Regulations
Q6. The following organizations or agencies are regulatory bodies that oversee the use of x-rays in medical imaging:
  U.S. Nuclear Regulatory Commission (NRC)
  Food and Drug Administration (FDA)
  National Council on Radiation Protection and Measurement (NCRP)
  U.S. Department of Transportation (DOT)
A. 1 only
B. 1 and 2
C. 1, 2, and 3
D. 1, 2, and 4
E. all of these are regulatory bodies

## Slide 78: Radiation Protection and Associated Regulations
Q7. As reported in NRCP Report 160, which category contributes the highest percentage to the total annual dose per capita?
A. computed tomography
B. nuclear medicine
C. radon
D. cosmic
E. medical

## Slide 79: Radiation Protection and Associated Regulations
Q8. Which of the following information is not needed to estimate the required shielding for a new x-ray room?
Which orientations the x-ray tube head can be placed in.
How many patients are seen in the x-ray clinic per week.
What types of exams are primarily done in that imaging suite.
The floor plans for the building design.
The number of people per week walking down the hallway adjacent to the x-ray suite.
A. #5 only
B. #3 only
C. #3 and #4
D. #4 and #5
E. all of this information is needed for shielding design

## Slide 80: Radiation Protection and Associated Regulations
Q9. What is the maximum permissible fluoroscopic exposure rate (normal mode) for an overhead tube configuration (e.g., urology imaging suite or multi-purpose R/F suite) and at what point is the exposure rate measured according to the Code of Federal Regulations (CFR)?
A. 10 R per minute, measured at the output window of the x-ray tube
B. 10 R per minute, measured at the entrance position of the patient (30 cm above the table top)
C. 10 R per minute, measured at the exit position of the patient (1 cm above the table top)
D. 20 R per minute, measured at the output window of the x-ray tube
E. 20 R per minute, measured at the entrance position of the patient (30 cm above the table top)

## Slide 81: Radiation Protection and Associated Regulations
Q10. The radiation badge typically worn by a radiologist is likely a/an
A. ionization chamber
B. scintillation detector
C. Geiger-Muller (GM) detector
D. optically stimulated luminescence (OSL) dosimeter

## Slide 82: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 83: X-ray Projection Imaging Concepts and Detectors
Q1. Which of the following exams would most likely be performed without the use of a grid?
A. PA chest
B. lateral lumbar spine
C. AP wrist
D. AP abdomen

## Slide 84: X-ray Projection Imaging Concepts and Detectors
Q2. Which of the following detectors is used in direct digital radiography?
A. gadolinium oxysulfide
B. cesium iodide
C. barium fluorohalide
D. amorphous selenium

## Slide 85: X-ray Projection Imaging Concepts and Detectors
Q3. In order to minimize the effect of geometric blur on a radiographic image you would:
set the highest mA and shortest exposure time available
select the small focal spot
chose the detector with the smallest available pixel size
utilize immobilization devices

## Slide 86: X-ray Projection Imaging Concepts and Detectors
Q4. Determine the actual size of an object if the image of the object measures 10 mm and the object is located half way between the x-ray tube target and the image receptor.
A. 1 mm
B. 5 mm
C. 15 mm
D. 20 mm

## Slide 87: X-ray Projection Imaging Concepts and Detectors
Q5. A portable x-ray is taken with a CR cassette with an 8:1 grid. The cassette is off-level from perpendicular to the x-ray tube. The resulting image will appear:
A. blurry
B. grainy
C. dark in the center
D. too light all over

## Slide 88: X-ray Projection Imaging Concepts and Detectors
Q6. If the distance from the x-ray tube to the image receptor is changed from 72” to 40”, which of the following will occur?
A. radiation dose to the patient will decrease by a factor of 4
B. image spatial resolution will increase
C. image noise will increase
D. the object of interest will appear larger on the image.

## Slide 89: X-ray Projection Imaging Concepts and Detectors
Q7. An increase in which of the following factors will increase image contrast?
A. kVp
B. filtration
C. SID
D. mAs

## Slide 90: X-ray Projection Imaging Concepts and Detectors
Q8. Which of the following will improve low- contrast resolution in a radiographic image?
A. change from a 10:1 to an 8:1 grid
B. move the patient closer to the image receptor
C. reduce mAs
D. use a smaller field of view

## Slide 91: X-ray Projection Imaging Concepts and Detectors
Q9. When the absorption efficiency in the phosphor layer of an x-ray detector is increased by making the phosphor layer thicker, which of the following occurs?
A. spatial resolution decreases
B. noise increases
C. contrast resolution decreases
D. patient dose increases

## Slide 92: X-ray Projection Imaging Concepts and Detectors
Q10. Which of the following uses a storage phosphor to capture the x-ray signal?
A. indirect DR
B. direct DR
C. computed radiography
D. film-screen radiography

## Slide 93: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 94: General Radiography
Q1. Which factor in a radiographic imaging system is responsible for the heart appearing enlarged on an AP chest image as compared to a PA chest?
the focal spot size
the use of focused grids
greater scatter from objects closer to the x-ray tube
the outward divergence of the x-ray beam from the focal spot
increased parallax from x-ray tubes with both large and small focal spots

## Slide 95: General Radiography
Q2. Portable x-ray images are generally inferior to those taken on stationary radiographic units. One of the reasons is that high-ratio grids are generally not used when acquiring portable radiographs, whereas they are used with stationary x-ray units. What is the reason for excluding high-ratio grid use for mobile radiography?
High-ratio grids have poorer scatter rejection than low ratio grids.
High-ratio grids are more difficult to align with the focal spot.
High -ratio grids are more easily mis-positioned upside down as compared with low-ratio grids.
Grids in general are not used in portable x-ray radiography as they increase exposure times.
One cannot manufacture high-ratio grids with short enough focal lengths.

## Slide 96: General Radiography
Q3. Which quantity is used to assess radiation risks to an individual organ that also incorporates the type of radiation involved?
A. absorbed dose (mGy)
B. equivalent dose (mSv)
C. effective dose (mSv)
D. kerma (mGy)
E. exposure (C/kg)

## Slide 97: General Radiography
Q4. Identify the artifact in this image.
a corrupted point in k-space
grid lines
interference pattern between grid lines and detector pixels
grid inserted upside down
patient motion

## Slide 98: General Radiography
Q5. In comparing screen-film to digital radiographic systems, which of the following statements is true?
Films can be overexposed, whereas digital systems are immune to overexposures.
Digital images always have higher signal-to-noise ratios (SNRs) than film images.
Film images generally have higher spatial resolution than digital images.
Digital image brightness and contrast can be adjusted by window and leveling. The same can be done with film by using a variable brightness view box.
Digitizing a radiographic film is equivalent to acquiring a digital image.

## Slide 99: General Radiography
Q6. Under automatic exposure control (AEC), increasing the SID from 40” to 72” in radiography results in
A. increased focal spot blurring
B. decreased focal spot blurring
C. an increase in patient exposure
D. noisier images
E. shorter exposure times

## Slide 100: General Radiography
Q7. List the following in terms of increasing effective dose:
1. abdomen
2. extremities
3. two view mammogram (both breasts)
4. posteroanterior chest
5. shoulder
A. 2, 1, 5, 4, 3
B. 5, 1, 3, 4, 2
C. 3, 4, 1, 2, 5
D. 4, 3, 1, 2, 5
E. 2, 5, 4, 3, 1

## Slide 101: General Radiography
Q8. A patient is five weeks pregnant and was referred for an x-ray examination of the pelvis. As the attending physician on duty, the technologist comes to you asking what she should do. What is the first step you should take before considering to proceed?
A. immediately cancel the exam unconditionally
B. re-confirm the pregnancy with a second pregnancy test
C. discuss the risks and benefits of the exam with the patient
D. discuss with the referring physician whether the exam is medically justified at this time
E. instruct the technologist to use a very low-dose technique

## Slide 102: General Radiography
Q9. What is the single most important component of a radiographic system for determining patient radiation dose?
focal spot size
x-ray generator power rating
x-ray generator type (3 phase, high frequency, falling load)
parameter settings of the automatic exposure control (AEC)
tabletop attenuation

## Slide 103: General Radiography
Q10. For a KUB on an average-sized patient, what would be a reasonable technique, taking into account the tradeoffs among patient dose, image contrast, image noise, and minimization of patient motion?
75 kVp, 400 mA, 50 ms
120 kVp, 800 mA, 15 ms
50 kVp, 100 mA, 500 ms
75 kVp, 100 mA, 25 ms
none of the above

## Slide 104: General Radiography
Q11. Assume radiographs are being acquired using automatic exposure control (AEC) at the level of the kidneys. In taking radiographs of a pregnant patient, what is the single most important thing that you could do to ensure the lowest dose to the fetus while maintaining, or even improving, image quality?
A. Use a high kVp since this will result in a lower mAs and decreased dose using AEC.
B. Wrap the patient’s abdomen in a lead apron to cover the fetus.
C. Collimate the x-ray field to cover the smallest area of anatomy required to be imaged.
D. Have the patient lie prone as opposed to supine on the examination table.
E. Remove the anti-scatter grid.

## Slide 105: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 106: Mammography
Q1. What kind of artifact is seen in this mammogram?
A. positioning
B. motion
C. contrast
D. noise

## Slide 107: Mammography
Q2. The left mammogram image shows motion artifact, and the right mammogram shows the corrected image. What was the change in acquisition parameter that resulted in a corrected image?
A. decreased compression
B. increased kVp
C. increased exposure time
D. increased mAs

## Slide 108: Mammography
Q3. What is your finding in the breast axillary region?
A. skin fold artifact
B. motion artifact
C. antiperspirant artifact
D. noise

## Slide 109: Mammography
Q4. The salt and pepper artifact effect caused in these images is due to _____?
A. over exposure
B. under exposure
C. motion
D. low contrast

## Slide 110: Mammography
Q5. In mammographic image acquisition, it is important to use an appropriate exposure time to ensure that the signal-to-noise ratio is higher so that signal and noise can easily be differentiated. In the following under exposed image, the artifact is due to_________.
A. high kVp used
B. placement of photo cell
C. motion
D. low contrast

## Slide 111: Mammography
Q6. In mammography, compression _____________
A. decreases x-ray scatter, increases geometric blurring
B. increases x-ray scatter, increases geometric blurring
C. decreases x-ray scatter, decreases geometric blurring
D. comforts the patient

## Slide 112: Mammography
Q7. During mammography acquisition, the cathode-anode axis is placed from the chest wall to nipple as shown. This helps to _________
A. achieve a more uniform exposure
B. maximize heel effect at chest wall
C. minimize motion
D. complete the process quickly

## Slide 113: Mammography
Q8. What is wrong with the following mammogram?
A. missing tissue
B. placement of photo cell
C. motion
D. low contrast

## Slide 114: Mammography
Q9. The following is an image of a mammography phantom. A typical ACR-approved mammography phantom contains __________.
A. 5 fibers, 5 speck groups, 5 masses
B. 6 fibers, 5 speck groups, 5 masses
C. 4 fibers, 5 speck groups, 5 masses
D. 5 fibers, 4 speck groups, 4 masses

## Slide 115: Mammography
Q10. In the CC view mammograms above, both of which were done on the same patient on the same day, there is more probability of missing the cancer on the left image because of _____.
A. low contrast
B. not enough tissue included near the chest wall
C. high contrast
D. wrong view

## Slide 116: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 117: Fluoroscopy and Interventional Imaging
Q1. Which of the following statements about fluoroscopic radiation dose is TRUE?
A. Fluoroscopic exposure time is the easiest metric to quantify and is therefore the best estimate for a patient’s fluoroscopic radiation dose.
B. Air Kerma at the reference point (Ka,r) is equivalent to the patient entrance skin dose if it is corrected for the inverse square effect.
C. Air Kerma Area Product (PKA), also known as the Dose Area Product, may be effectively used for estimating stochastic risk rather than deterministic risk for the exposed patient.
D. Peak Skin Dose (PSD or Dskin,max) can be easily and accurately calculated in real time and is an effective metric for predicting deterministic skin injuries following fluoroscopic exposure.
E. Prolonged fluoroscopy with cumulative dose exceeding 15 Grays over all exposed fields is considered a sentinel event.

## Slide 118: Fluoroscopy and Interventional Imaging
Q2. Which of the following non-deterministic tissue effects should be considered for a fluoroscopic procedure resulting in high, single-site acute skin doses?
erythema (skin reddening)
epilation (hair loss)
desquamation
dermal necrosis
carcinogenesis

## Slide 119: Fluoroscopy and Interventional Imaging
Q3. Additional dose-management actions are recommended after thresholds for a substantial radiation dose level (SRDL) are exceeded. Which of the following thresholds should a fluoroscopist pay attention to?
peak skin dose exceeding 3 Grays.
dose to a single field exceeding 1500 rads (15 Grays).
fluoroscopy time exceeding 60 minutes.
reference air kerma exceeding 5 Grays.
air kerma area product exceeding 500 Gy cm2.
Pay attention to threshold ii only.
Pay attention to threshold i for deterministic effects and v. for stochastic effects only.
Exceeding any one of the thresholds should initiate dose management actions.
Any three of the five thresholds must be exceeded before dose management actions.
All of the five thresholds must be exceeded before initiating dose management actions.

## Slide 120: Fluoroscopy and Interventional Imaging
Q4. It is important for the fluoroscopist to know the operational settings of the system being used. In general, fluoroscopic systems can be operated with automatic exposure control (AEC), but the exposure level or the pulse rate may be selected in order to minimize patient exposures. Arrange the following fluoroscopic settings in terms of DECREASING patient exposure. (pps = pulses per second)
Pulsed, High Level, 30 pps
Pulsed, 15 pps
Continuous
Cine
i, ii, iii, iv
iv, iii, ii, i
iii, iv, i, ii
iv, iii, i, ii
ii, i, iv, iii

## Slide 121: Fluoroscopy and Interventional Imaging
Q5. Which of the following is an example of POOR clinical practice with fluoroscopy?
requiring the use of radiation dosimeters and personal protective equipment (e.g., aprons, neck shields, etc.) for all personnel in the fluoroscopic use room
positioning the image receptor as close to the patient surface and the x-ray tube as far from the patient surface as possible
selecting the appropriate magnification mode and using collimation to only irradiate the area or organ of interest
placing a lead apron in the radiation field to reduce exposure in other areas of the patient
enabling system features, such as last image hold (LIH) and pulsed fluoroscopy, if applicable

## Slide 122: Fluoroscopy and Interventional Imaging
Q6. Artifacts in fluoroscopy can be highly dependent on the type of image receptor being used. Respectively, image intensifier (II) type image receptors are susceptible to a/an ________ artifact, while flat panel type image receptors are susceptible to a/an __________ artifact.
pincushion distortion; dead-pixel drop-off
beam hardening; digital reconstruction
quantum mottle’ brightness gain
gray scale saturation; vignetting
persistence; s-distortion

## Slide 123: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 124: CT
Q1. What is the artifact identified by the arrow in the body CT image shown here?
A. patient motion
B. aliasing
C. beam hardening
D. detector failure

## Slide 125: CT
Q2. Which of the following actions would you take to minimize or eliminate the artifact identified by the arrow in the pelvic CT shown here?
A. perform an air calibration
B. increase pitch
C. increase beam collimation
D. increase kVp

## Slide 126: CT
Q3. Use of which of the following reconstruction options would improve visibility of low-contrast structures in this figure?
A. lung filter
B. bone filter
C. soft tissue filter
D. thinner reconstructed slice width.

## Slide 127: CT
Q4. Which of the following would improve visibility of low-contrast structures in this image without increasing radiation dose to the patient?
A. increase mA
B. increase tube rotation time
C. increase reconstructed slice width
D. increase kVp

## Slide 128: CT
Q5. The artifact indicated by the arrow in this image is the result of:
A. patient motion
B. beam hardening
C. poor detector calibration
D. partial volume averaging

## Slide 129: CT
Q6. The artifact indicated by the arrow on this image may develop in which type of CT scanner?
A. electron beam CT
B. rotate-translate
C. rotate-rotate
D. rotate-stationary

## Slide 130: CT
Q7. Spatial resolution in this figure could be improved by:
A. using wider collimation
B. reducing the field of view
C. increasing pitch
D. application of a soft tissue reconstruction filter

## Slide 131: CT
Q8. What difference in CT number (HU) is expected between tissue A and tissue B as shown in this figure?
A. 0
B. 500
C. 1000
D. 2000

## Slide 132: CT
Q9. The automatic exposure control system on a CT scanner determines the tube current for a particular scan based on a planning view (scout) image acquired with the tube stationary under the patient’s bed. If the patient centerline is positioned below scanner isocenter, which of the following will be reduced?
A. spatial resolution
B. low-contrast visibility
C. image noise
D. patient dose

## Slide 133: CT
Q10. The automatic exposure control system on a CT scanner determines the tube current for a particular scan on a planning view (scout) image acquired with the tube stationary over the patient’s bed. If the patient centerline is positioned below scanner isocenter, which of the following will increase?
A. spatial resolution
B. low-contrast visibility
C. image noise
D. patient dose

## Slide 134: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 135: Ultrasound
Q1. What is the artifact in this image with Adenomyomatosis clinical condition?
mirror image artifact
reverberation artifact
comet tail or ring down artifact

## Slide 136: Ultrasound
Q2. What is the name of the artifact seen with bowel gas?
comet tail
mirror image
dirty shadowing, or dirty acoustic shadowing

## Slide 137: Ultrasound
Q3. What is the name of the artifact that occurs when the Doppler sampling rate is less than twice the Doppler frequency shift? (Hint: this artifact causes the high-frequency components to wrap around from the positive extreme of the scale to the negative extreme.)
aliasing
mirror image
reverberation

## Slide 138: Ultrasound
Q4. A simple cyst is defined as an anechoic structure with imperceptible walls and what property illustrated here? (Hint: this occurs because fluid-containing structures attenuate sound much less than solid structures.)
shadowing
posterior enhancement
refraction

## Slide 139: Ultrasound
Q5. This ultrasound image has an artifact with the arrow pointing to it. Name this artifact.
A . mirror-image artifact
B. ring artifact
C. banding artifact

## Slide 140: Ultrasound
Q6. In these two ultrasound images, the top image is done without harmonics, and the bottom image is done with harmonics. The result is to achieve:
enhancement in spatial resolution
enhanced contrast
Doppler shift

## Slide 141: Ultrasound
Q7. Body habitus and transducer selection play key roles in ultrasound imaging. In these images, the selection of a curvilinear transducer instead of a linear transducer gives _____.
better image depth
better resolution
more field of view

## Slide 142: Ultrasound
Q8. How can the artifact shown in this image be corrected?
adjustment of the color Doppler threshold
adjustment of the color scale
adjustment of the color gain
adjustment of the sample volume angle to align with the wall contour of the ICA

## Slide 143: Ultrasound
Q9. For a better evaluation of the ECA on the Doppler study shown here, what should be adjusted?
color Doppler sampling window
color scale
color gain
sample volume angle to be aligned with the wall contour of the ICA

## Slide 144: Ultrasound
Q10. Using Doppler to interrogate a vessel demands using the correct angle. An angle of ____ degrees is usually preferred to obtain accurate velocity measurements.
80
65
60
30

## Slide 145: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 146: MRI
Q1. What artifact is present in this MR image?
A. patient motion
B. aliasing
C. truncation
D. flow artifacts

## Slide 147: MRI
Q2. Which of the following techniques will you use to remove the aliasing artifacts without changing spatial resolution or scan time in this figure, a high-resolution T2W sagittal image? Orbits are the subject.
A. increase FOV
B. increase FOV and matrix size
C. reposition the patient to make the orbits at the center of the FOV
D. use anti-aliasing technique, such as No Phase Wrapping

## Slide 148: MRI
Q3. Which of the following techniques could be used to reduce this artifact?
A. gradient echo sequence
B. spin echo sequence
C. increase TE, decrease receiver bandwidth
D. short TE, increased bandwidth
E. both B and D

## Slide 149: MRI
Q4. What artifact is present in the following MRI image?
A. motion artifact
B. flow artifact
C. RF interference artifact
D. gradient failure artifact

## Slide 150: MRI
Q5. What is the most likely interpretation of the following MR image?
A. T1W abdominal image
B. T1W abdominal image with poor fat suppression and some breathing artifacts
C. T2W abdominal image with poor fat suppression and some breathing artifacts
D. T2W abdominal image

## Slide 151: MRI
Q6. This figure is an MR pulse sequence timing diagram. What pulse sequence is it?
A. spin echo (SE) sequence
B. gradient echo (GRE) sequence
C. fast spin echo (FSE) sequence
D. echo planar imaging (EPI) sequence

## Slide 152: MRI
Q7. Although spin echo sequence is kind of slow, it is still a classic MRI technique generating good image contrast with minimal artifacts. Which of the following parameters can be combined to generate T1-weighted brain image using spin echo sequence on 1.5T system?
A. TR = 100 msec, TE ~10 msec
B. TR = 400600 msec, TE ~10 msec
C. TR  2000 msec, TE ~10 msec
D. TR  2000 msec, TE  80 msec

## Slide 153: MRI
Q8. The following figure shows a T2W brain image. Which of the following parameters can be combined to generate T2-weighted brain image using spin echo sequence?
A. TR = 100 msec, TE ~10 msec
B. TR = 400- 600 msec, TE ~10 msec
C. TR  2000 msec, TE ~10 msec
D. TR  2000 msec, TE  80 msec

## Slide 154: MRI
Q9. This is a fast spin echo (FSE) sequence timing diagram, with 4 echo train length (ETL) plotted and an example of how the k-space is filled. For a 256 x 256 image, SE acquisition takes 4 minutes. How long will it take for this FSE acquisition?
A. 4 min.
B. 8 min.
C. 1 min.
D. 16 min.

## Slide 155: MRI
Q10. Assume a MRI image is acquired by the FSE sequence diagrammed in the figure above where TR = 500 msec. What image contrast will it most likely generate?
A. T1W
B. T2W
C. Proton density weighted (PD)
D. T2* weighted

## Slide 156: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine

## Slide 157: Nuclear Medicine
Q1. What is the mechanism of localization of Tc-99m MAA?
A. capillary blockade
B. diffusion
C. phagocytosis
D. sequestration

## Slide 158: Nuclear Medicine
Q2. What is the mechanism of localization of Tc-99m methylene diphosphonate (MDP)?
capillary blockade
chemisorption
diffusion
metabolism

## Slide 159: Nuclear Medicine
Q3. What is the mechanism of localization of I-123 sodium iodide in the thyroid gland?
active transport
diffusion
metabolism
receptor binding

## Slide 160: Nuclear Medicine
Q4. What is the mechanism of localization of F-18 fluorodeoxyglucose (F-18 FDG)?
active transport
diffusion
compartmental localization
receptor binding

## Slide 161: Nuclear Medicine
Q5. Excessive Mo-99 in the Tc-99m pertechnetate eluate is an example of a problem with:
physical purity
radionuclidic purity
radiochemical purity
chemical purity

## Slide 162: Nuclear Medicine
Q6. What is the regulatory limit for the amount of Mo-99 per mCi of Tc-99m radiopharmaceutical at the time of administration?
0.15 microcurie (uCi)
0.5 uCi
0.15 millicurie (mCi)
0.5 mCi

## Slide 163: Nuclear Medicine
Q7. Too much aluminum in the Mo-99/Tc-99m eluate is an example of a problem with:
physical purity
radionuclidic purity
radiochemical purity
chemical purity

## Slide 164: Nuclear Medicine
Q8. What is the regulatory limit of aluminum oxide (Al2O3) in the Mo-99/Tc-99m generator eluate?
<10 ug/ml
<20 ug/ml
<10 mg/ml
<20 mg/ml

## Slide 165: Nuclear Medicine
Q9. What is the regulatory limit by the NRC for error between the indicated exposure rate and the calculated exposure rate for survey instruments?
10%
20%
25%
50%

## Slide 166: Nuclear Medicine
Q10. How often should the dose calibrator be tested for accuracy?
weekly
monthly
quarterly
annually

## Slide 167: Nuclear Medicine
Q11. How often should the dose calibrator be tested for constancy?
A. daily
B. weekly
C. monthly
D. quarterly

## Slide 168: Nuclear Medicine
Q12. How often should the dose calibrator be tested for linearity?
daily
weekly
monthly
quarterly

## Slide 169: Nuclear Medicine
Q13. A patient with a history of thyroid cancer has suspected bone metastases in the cervical spine. It is recommended to perform both an I-123 radioiodine scan as well as a bone scan using Tc99m MDP. Which would be the optimum sequence to perform unambiguous imaging in the shortest time?
Administer the I-123 and Tc 99m simultaneously Perform the bone scan first and recall the patient after 24 hours for the radioiodine scan.
Administer the I-123 first . Perform the I-123 scan at 24 hours then inject Tc 99m MDP and perform the bone scan at 4 hours.
Administer the I-123 first and scan at 24 hours. Ask the patient to wait for three days, and then administer the Tc99m and do the bone scan.
Administer the Tc 99m MDP first. Perform the bone scan. Then administer the I-123 and perform the thyroid workup after 24 hours.
Administer the Tc99m MDP, followed shortly thereafter by the I-123. Perform the bone scan at 4 hours and the thyroid workup at 24 hours.
Administer the Tc 99m MDP first. Perform the bone scan. Have the patient return the next day and administer the I-123 and perform the thyroid workup after 24 hours.

## Slide 170: Nuclear Medicine
Q14. The source shown would be used for:
A. daily check of survey meter
B. dose calibrator linearity
C. calibration of well counter
D. dose calibrator accuracy
E. intrinsic uniformity test of scintillation camera

## Slide 171: Nuclear Medicine
Q15. This Tc-99m macroaggregated albumin shunt study demonstrates:
A. radionuclidic impurity
B. chemical impurity
C. radiochemical impurity
D. pharmaceutical impurity

## Slide 172: Nuclear Medicine
Q16: A Gallium scan is performed and a representative image is shown. The acquisition was fixed time, and the number of counts obtained were as expected. This could be caused by:
A. use of the wrong collimator
B. an incorrect window
C. a photomultiplier tube that needs retuning
D. an incorrect uniformity map

## Slide 173: Index
Beginning of File
Structure of the Atom
Electromagnetic Radiation
Particulate Radiation
Interactions
Radiation Units
X-Ray Production
Imaging Science & Technology
Biological Effects
Radiation Protection
Projection Imaging
General Radiography
Mammography
Fluoroscopy / Interventional
Computed Tomography
Ultrasound
Magnetic Resonance Imaging
Nuclear Medicine